Location Routing Number (LRN) Selection Criteria

LRNs are 10 digit numbers that are assigned to network switching elements (Central Office - Host and Remotes as required) for routing of calls in the network.  Changes in the regulatory, technical or business environment may necessitate modifications to these LRN selection criteria.

- The first six digits of the LRN shall be one of the assigned NPA/NXXs that is activated and resident in the switching element. An LRN may have to be changed due to switch replacements, CO code moves, LERG reassignments, NPA Splits, or NPA Boundary realignments.

- All local service providers (including LECs and WSPs) who port numbers into their networks shall select at least one LRN for each Local Number Portability (LNP) capable recipient switch.

- Where an LNP capable recipient switch is used to serve more than one ILEC exchange, at least one LRN shall be selected for each ILEC exchange area served by that switch and in which LNP is provided by that switch.

- A local service provider receiving a ported number must assign to that ported number an LRN associated with the ILEC exchange area in which the number resides.

- The last 4 digits of the 10 digit LRN may be selected at the discretion of the local service provider.  It is recommended that a working telephone number should not be selected as an LRN.